## Slide 1: Parallelized Kalman-Filter-Based Reconstruction of Particle Tracks on Many-Core Processors and GPUs
August 31, 2017
G. Cerati4, P. Elmer3, S. Krutelyov1, S. Lantz2, M. Lefebvre3,
M. Masciovecchio1, K. McDermott2, D. Riley2, M. Tadel1, P. Wittich2,
F. Würthwein1, A. Yagil1
University of California – San Diego
Cornell University
Princeton University
Fermilab

## Slide 2: Outline
Problematic & experimental setup
Overview of the parallelization on x86 processors
  Sandy Bridge and Knights Corner
Parallelizing on GPUs
  Porting Strategy
  Data structures
  Track fitting: lessons learned
  Track building: increasing the algorithmic complexity
  Optimizing data transfer
  Alternative parallelization scheme
  First results on P100
  Issues

## Slide 3: Why Parallelizing?
By 2025, the instantaneous luminosity of the LHC will increase by a factor of 2.5, transitioning to the High Luminosity LHC
Increase in detector occupancy leads to significant strain on read-out, selection, and reconstruction
Clock speed stopped scaling
Number of transistors keeps doubling every ~18 months
Multi-core architectures
  E.g. Xeon, MIC, GPUs

## Slide 4: KF Track Reconstruction
Tracking proceeds in three main steps: seeding, building, and fitting
In fitting, hit collection is known: repeatedly apply the basic logic unit
In building, hit collection is unknown and requires branching to explore many possible candidate hits after propagation

## Slide 5: Experimental Setting
Simplified setup
Detector conditions
  10 barrel pixel layers, evenly spaced
  Hit resolution
    σx,y = 100μm
    σz = 1.0mm
  Constant B-field of 3.8T
  No scattering/energy loss
Track conditions
  Tracks generated with MC simulation uniformly in η,φ (azimuthal angle), and pT
  Seeding taken from tracks in simulation
Realistic Setup
Options to add material effects, polygonal geometry:
More realistic setup partially built:
Barrel and Endcap (x86 only)
Notes: We are not going to talk about the realistic setup as it is not implemented for GPU.

## Slide 6: Selected Parallel Architectures
 | Xeon E5-2620 | Xeon Phi 7120P | Tesla K20m | Tesla K40
Cores | 6 x 2 | 61 | 13 | 12
Logical Cores | 12 x 2 | 244 | 2496 CUDA cores | 2880
Max clock rate | 2.5 GHz | 1.333 GHz | 706 MHz | 745 MHz
GFLOPS (double) | 120 | 1208 | 1170 | 1430
SIMD width | 64 bytes | 128 bytes | Warp of 32 | Warp of 32
Memory | ~64-384 GB | 16 GB | 5 GB | 12 GB
Memory B/W | 42.6 GB/s | 352 GB/s | 208 GB/s | 288 GB/s

## Slide 7: Challenges to Parallel Processing
Vectorization
  Perform the same operation at the same time in lock-step across different data
  Challenge: branching in track building - exploration of multiple track candidates per seed
Parallelization
  Perform different tasks at the same time on different pieces of data
  Challenge: thread balancing – splitting the workload evenly is difficult as track occupancy in the detector not uniform on a per event basis
KF tracking cannot be ported in straightforward way to run in parallel
Need to exploit two types of parallelism with parallel architectures
Vectorization

## Slide 8: Matriplex
Matrix operations of KF ideal for vectorized processing: however, requires synchronization of operations
  Arrange data in such a way that it can loaded into the vector units of Xeon and Xeon Phi with Matriplex
  Fill vector units with the same matrix element from different matrices: n matrices working in synch on same operation
Matrix size NxN, vector unit size n
fast memory direction
vector
unit
Notes: Matriplex, Multiple track cands slides are important not only to introduce the slide with CPU/MIC results but also to introduce the data struct and algorithm; making it easier to understand what had to be done on the GPU side.

## Slide 9: Handling Multiple Track Candidates: First Approach
propagate candidate to layer
loop over hits in window
test χ2 < cut
go to next hit
sort temp vector, and
clean copies > N
fail
pass
candidates ready
for next layer
all candidates in layer
for all seeds processed
N.B. When processing tracks in parallel with Matriplex, copy + update forces other processes to wait!
 We need an other approach
copy candidate
update with hit
push into temp vector
χ2?
χ2?
Fail
χ2?
Pass
Pass
χ2?
Pass

## Slide 10: Optimized handling of multiple candidates: “Clone Engine”
propagate candidate to layer
loop over hits in window
test χ2 < cut
go to next hit
add entry in bookkeep list
sort bookkeep list,
copy only the best N
fail
pass
candidates still
need update
all candidates in layer
for all seeds processed
update candidate with hit from previous step
N.B. Clone Engine approach should (and does) match physics performance of previous approach!

## Slide 11: Track Building: Sandy Bridge and KNC
Toy Monte Carlo experiment
  Simplified geometry & simulated events
  Similar trends in experiments with realistic geometry & CMSSW events
Scaling tests with 3 building algorithms
  Best Hit - less work, recovers fewer tracks (only one hit saved per layer, for each seed)
  Standard & Clone Engine - combinatorial, penalized by branching & copying
Two platforms tested
  Sandy Bridge (SNB): 8-float vectors, 2x6 cores, 24 hyperthreads
  Knights Corner (KNC): 16-float vectors, 60+1 cores, 240 HW threads
Vectorization - speedup is limited in all methods
  Faster by only 40-50% on both platforms
Multithreading with Intel TBB - speedup is good
  Clone Engine gives best overall results
  With 24 SNB threads, CE speedup is ~13
  With 120 KNC threads, CE speedup is ~65
Sandy Bridge
KNC
Vectorization
Multithreading
Notes: Only show Toy MC because it’s the only thing we can show on the GPU. Showing many unrelated things may be confusing

## Slide 12: GPU: Finding a Suitable Memory Representation
“Linear”
”Matriplex”
same strategy as the
one used for CPUs’
vector units.
Memory
Array
Threads
Notes: Non-shared linear version 2 orders of magnitude slower
Coalescent accesses / Aligned data accesses (padded allocation) = group 32 glob. memory accesses together / glob mem access 200-400 cycles

## Slide 13: GPU Porting Strategy: An Incremental Approach
Start with fitting:
  Share a large number of routines with building
  Simpler: less branching, indirections, ….
  Draw lessons along the way
Gradually increase complexity
  ”Best Hit”: (at most) 1 candidate per seed
    New issues: Indirections, Numerous memory accesses
  “Combinatorial”: multiple candidates per seed
    New issues: Branching
Notes: New issues: not “new” per say, “

## Slide 14: Fitting: Optimizing Individual Events
GPU: K40
Pre-optimization
Better data access: use read only-cache (const __restrict__)
Merging kernels (reducing launch overhead)
Use registers over shared memory
Chart: Overall Kernel Time (ms)
| 1.0 | 2.0 | 3.0 | 4.0
Overall Kernel time | 69.95 | 36.457 | 12.268 | 8.5999
10 events @ 20k tracks
For each event:
  Reorganize tracks
  Transfer tracks
  For each layer:
    Reorganize hits
    Transfer hits
    Compute
    Transfer partial result back
CPU
GPU
Propagation & Update
Computations
Reorganizing data to Matriplex
Numerous indirections
Notes: Once the proper data structure as been determined, track fitting has been ported to GPU.
Since debugging is particularly unpleasant on the GPU, the process has been to gradually port existing CPU routines to the GPU. This helps checking that everything is working each time something is modified.
Of course, it implies adding CPU/GPU data transfers around each routine and forbid any insights as what the performance of the final port might be.
1.
At some point, all temporary data transfers are removed and only happen at the beginning and at the end of the the fitting process.
This is the initial bar, showing a time of 70ms to fit 10 events of 20K each on a Nvidia Tesla K40 GPU.
2.
From there, the optimization process can begin.
As it has been outlined early one, proper data accesses are critical.
Recent GPUs (at least the ones dedicated to HPC) have read-only cache for data stored in global-memory. It is very similar to what the texture memory and cached were used for; but much simpler to use).
Using this read-only cache, among other things gives a 2-fold improvement.
3.
Kernels (GPU functions called from the CPU) have a limited size and called a large number of time.
This has two undesirable effects
Launching a kernel has some overhead.
Data has to be re-read from global-memory each time a new kernel is launched.
Merging kernels and reducing the number of kernel calls alleviate both issues.
This gives further improvements (bar 3)
4.
Initial kernels were using shared memory (similar to an explicit L2 cache) to store data used several times somewhere closer to the core than global memory.
Usually shared memory is the most useful when data has to be shared between threads of a same block (hence the name).
Going with registers instead shared memory brings some additional gains.

## Slide 15: Fitting: Filling up the GPU
Chart: Time to fit 10 events @ 200k tracks
| 1000 | 8000 | 10000 | 16000 | 32000 | 100000 | 200000
5 threads | 95 | 26.5 | 25 | 26.5 | 32 | 32.3 | 34.2
10 threads | 116 | 35.5 | 28 | 33.3 | 26.54 | 33.1 | 29.3
1 threads | 177 | 76.6 | 55 | 75 | 53 | 76.5 | 120
GPU: K40
Larger Matriplex size
  Faster kernels
  Longer reorganization
Smaller Matriplex size
  “Faster” reorganization
Concurrent events, different streams
  Individual kernel instances take longer
  Overall time shorter
Compromise:
  Find Matriplex size so that time(reorg + transfer + kernel) is minimum

## Slide 16: Track Building: GPU Best Hit
Parallelization: as in Track Fitting
  Parallelization: 1 GPU thread per candidate
Reorganizing on the CPU is not an option for building
  Frequent reorganizations  very small kernels
  Numerous reorganizations no more overlapping possible
Data Structures
  Matching CPU and GPU data structures to ease data transfers
    Later reorganized as Matriplexes on the GPU
  Static containers directly used on the GPU: Hits, Tracks, …
  Object composition forces additional trick for classes at the top of the wrapping hierarchy
    Keep arrays of sub-objects both on the host and on the device to be able to fill copy sub-objects from the CPU and access them from the GPU.
    Data transfer overhead from transferring multiple smaller objects

## Slide 17: Track Building: Tuning Parameters
Usual problem, find tmin that satisfies:
  tmin = min f(a, b, c, d)
  (a) Number of Eta bins (*)
  (b) Threads per block
  (c) Matriplex width
  (d) Number of tracks per event
”Standard” insight
  “Limited” number of tracks is penalizing
  Even more so with newer GPUs
  Computing multiple events concurrently is mandatory
Chart: Number of Eta bins
| 21.0 | 17.0 | 13.0 | 9.0 | 5.0 | 1.0
K20 | 0.46425 | 0.38305 | 0.3003 | 0.21918 | 0.20232 | 0.16824
P100 | 0.25782 | 0.20195 | 0.1653 | 0.11043 | 0.06739 | 0.04368
Chart: Matriplex Size
| 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32768.0
K20 | 55.463 | 30.82 | 17.4221 | 10.0989 | 5.43 | 2.9638 | 1.6392 | 0.84173 | 0.43428 | 0.23166 | 0.14586 | 0.12158 | 0.12228
P100 | 24.0634 | 13.3677 | 7.41 | 4.1303 | 2.3339 | 1.3472 | 0.82455 | 0.46467 | 0.24233 | 0.13213 | 0.07593 | 0.04979 | 0.0434
10 events @ 200k tracks
(*) Eta bins: Hits are binned by η to reduced the amount of hits that should be tried for a track .
10 events @ 20k tracks
0.043 s
0.043 s
0.17
0.12

## Slide 18: Building with Multiple Candidates: “GPU Clone Engine”
propagate candidate to layer
loop over hits in window
test χ2 < cut
go to next hit
add entry in sorted
bookkeep list
Merged sorted bookkeep lists,
copy only the best N
fail
pass
candidates still
need update
all candidates in layer
for all seeds processed
update candidate with hit from previous step
N.B. Clone Engine approach should (and does) match physics performance of previous approach!
Notes: Now that we get the “best hit” working we can have a look at the more challenging problem of combinatorial track building. Which is actually the one of interest.
Forced to keep the lists sorted to avoid size growth.

## Slide 19: Building with Multiple Candidates
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
0 |  |  |  | 1 |  |  |  | 2 |  |  |  | 3 |  |  |  | 4 |  |  | 
0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 3
itrack
iseed
icand
ithread
BlockDim.x
MaxCandsPerSeed
MaxCandsPerSeed = 4
BlockDim.x = 8
Global Mem.
Old Candidates
Share Mem.
New Candidates*
Fast-dim
A Clone-Engine approach is required:
  Moving tracks around global memory is guaranteed to be a performance killer
Parallelization: 1 thread per candidate
  Other strategies should be investigated (e.g. 1 thread per seed)
*Potential next-layer candidates, after adding an acceptable hit from the current layer

## Slide 20: Track-based parallelization
1 seed, 4 candidates processed concurrently
4 sets of new candidates
Reduced into 1 set of new candidates
“Map-Reduce-Scatter”
Synchronization across blocks
First layers: only a few candidates per seed for the first layers
idle threads
Also doing concurrent events to better fill the device
sync
sync
sync

## Slide 21: Track Building: Initial Performance
Chart: Track Building: Best Hit
| 10 events @ 20k tracks
SNB 1 thr, AVX | 0.4475
SNB 24 thr, AVX | 0.037
K40 + transfers | 0.14
Chart: Track Building: Clone Engine
| 10 events @ 20k tracks
SNB 1 thr, AVX | 6.08
SNB 24 thr, AVX | 0.43
K40 + transfers | 4.97
20K tracks per event is not enough to give good performance
Need to increase the number of events concurrently fed to the GPU by using different streams
Too many synchronizations
Sorting’s branch predictions
Idling threads when number of candidates per seed is not maximum
Transfer account for 46% of the time

## Slide 22: Data Transfer Optimization

## Slide 23: Clone Engine: Timeline
(1) Memcpy > Compute
(2) Zooming in:
  Many small transfers
  Latency is high
  Even if asynchronous
(3) Transfer size:
  Ridiculously small
1
2
3

## Slide 24: Transfer segmentation / Hierarchical data structure
EventCombCand
EtaBinCombCand
vector <vector <>>
vector <Tracks>
vector <Tracks>
vector <Tracks>
EventCombCand
EtaBinCombCand
Tracks[]
…
CPU
GPU
1..1
1..1
1..1
Data transfers

## Slide 25: Temporary Array
EventCombCand
EtaBinCombCand
vector <vector <>>
vector <Tracks>
vector <Tracks>
vector <Tracks>
EventCombCand
EtaBinCombCand
Tracks[]
…
Tracks[]
“Single” device to host copy
Move / Copy

## Slide 26: Timeline after transfer bundling

## Slide 27: Going Fortran (≤ 77)
Hit[]
Bin[]
LayerOfHitsCU
…
EventOfHitsCU
Allocate one big array
  On CPU and GPU
Flatten the structure
Bundle transfers
  Pre-copy small vectors into the large CPU array
Layers point to these large arrays

## Slide 28: Going back from Fortran
Hit[]
Bin[]
LayerOfHitsCU
…
EventOfHitsCU
DeviceBundle
  Has a DeviceVector
    Avoid spurious alloc / free
    Std::Vector::reserve() like operation  reuse allocated array for subsequent events
DeviceArrayView
  Does not have its own memory
  Points to a DeviceBundle part

## Slide 29: Timeline after Fortran (1 CPU Thread

## Slide 30: Does it allow events to overlap?
4.97
CtD 1 thread | 4.97 s
1 thread | 3.03 s
4 threads | 2.01 s
Quadro K6000 / Tesla K40

## Slide 31: GPU Parallelization Tracks vs. Seeds

## Slide 32: Seed-based parallelization
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
i | i | i | i | i | i | i | i | i | i | i | i | i | i | i | i | i | i | i | i
iseed
icand
itrack = iseed*maxCandsPerSeed + icand
ithread
MaxCandsPerSeed = 4
BlockDim.x = 8
Global Mem.
Old Candidates
Fast-dim
For loop over icand and update heaps.
Heaps are independent
Still in SM
No Sync required (no merge)
Less threads, but more computations per thread
Can we gain something:
Higher compute/mem access ratio ?
Ability to launch concurrent events more efficiently?

## Slide 33: Track-based / Seed-based Comparison
 |  | Track-based | Seed-based
1 thread | Event-Loop | 3.037 | 3.25
 | Kernel | 1.58 | 1.795
 | HtoD | 0.452 | 0.449
 | DtoH | 0.054 | 0.054
4 threads | Event-Loop | 2.26 | 2.58
 | Kernel | 1.58 | 1.91
 | HtoD | 0.744 | 0.758
 | DtoH | 0.114 | 0.115
10 threads | Event-Loop | 2.08 | 2.33
 | Kernel | 1.62 | 2.03
 | HtoD | 0.786 | 0.856
 | DtoH | 0.112 | 0.118
20 events @ 10K tracks, from file, Quadro K6000

## Slide 34: P100 / Broadwell comparison
P100 + Broadwell CPU, PCI-e connection
Seed-based algorithm works better on Pascal
“Scales” better with the number of CPU threads
  Track-based freezes when number of CPU threads > 5
  Does not freeze on the K6000
  Probably due to slurm

## Slide 35: P100, streaming, overlapping
P100-PCIe 200ev @ 10k tracks, 40 CPU threads

## Slide 36: Issues (Some)
Latency
Branching
  If hit better than worst of current bests
  Maintaining heap property: left / right dichotomy
Shared memory
  Heaps are too big: 34kB for blocks of 256 threads
    Heaps in global mem for track-based algorithm ?
    Heap in local mem for seed-based algorithm ?
  Hits from hit-loop in SM?
    All candidates loops over the same
Track-based heap-merge synchronization
  New ”thread_group.sync” in CUDA 9?